## Slide 1
Prepared by:
Syed Yousaf Munib (6933767)
Supervisor: Dr. Bahman Amini Horri
Next Generation Green Hydrogen from UK Offshore Wind
1
Course: Research Dissertation (ENGM083)
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk

## Slide 2
RESEARCH AIM
1
Evaluate PEM water electrolysis for green hydrogen production using UK offshore wind energy.
2
Compare PEM performance with alkaline and solid oxide electrolyser technologies.
3
Design a complete offshore system, seawater treatment, hydrogen production, compression, storage (350 bar) and transportation.
4
Assess techno economic feasibility CAPEX, OPEX, and payback period.
PROBLEM STATEMENT
1
Design gap: No integrated offshore hydrogen system discuss.
2
Technology Gap: No Justified electrolyser selection for offshore.
3
Simulation gap: Variable wind impact on hydrogen output unknown.
4
Economic gap: CAPEX, OPEX & Payback not assessed with storge and transportation.
Aim and Problem Statement
Course: Research Dissertation (ENGM083)
2
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk

## Slide 3
Objectives & Key Insights
Objective 01
Objective 02
Design system:
Seawater treatment, PEM electrolysis, hydrogen compression, Storage and transportation.
Objective 03
Simulate:
Aspen HYSYS simulation model and perform mass and energy balance calculations.
Objective 04
Techno economic analysis:
CAPEX, OPEX, and payback period including the effect of hydrogen storage and transportation.
KEY INSIGHT : PEM Suitability for Offshore Hydrogen
50-80 °C
Operating Temp.
Low temperature and suitable for offshore platforms.
Fast
Response Time
Rapid response to variable wind power input.
>99.9%
H₂ Purity
High purity output meets storage requirements.
350 bar
Storage Target
Commercially viable compressed H₂ storage.
Objectives and Key Insights
Course: Research Dissertation (ENGM083)
3
Sources: (Aminaho et al.,2025; Ibrahim et al., 2022 )
Compare and select:
Review alkaline, PEM, solid oxide electrolyser and justify the selection of PEM.

## Slide 4
Comparison of electrolyser Technologies: Three main electrolyser technologies are identified in the literature. PEM is selected for this study due to its suitability for variable offshore wind power.
Parameter
Alkaline (AWE)
PEM ✓
Solid Oxide (SOEC)
Maturity
High (commercial)
High (commercial)
Low-medium
Operating Temp.
60-90 °C
50-80 °C
700-1000 °C
Efficiency
60-75%
65-80%
70-90%
Dynamic Response
Slow
Fast
Poor
H₂ Purity
Moderate
Very High
High
Water Quality
Moderate
High purity
High purity
Capital Cost
Low
Medium
High
Offshore Suitability
Moderate
High
Low
Sources: (Aminaho et al.,2025; Carmo et al., 2013; Niblett et al., 2024)
Literature Review
Course: Research Dissertation (ENGM083)
4
Table 1: Comparison of electrolyser technologies.

## Slide 5
Sources: (Ibrahim et al., 2022; Rezaei et al., 2024; Travaglini et al., 2025)
Comparison of offshore and onshore
Course: Research Dissertation (ENGM083)
5
Figure 1: Comparing offshore and onshore hydrogen production.
Parameter | Offshore Production | Onshore Production
Location | Near offshore wind farms | On land, grid-connected
Elec. Transmission | Not required | Required (2–5% losses)
Energy Efficiency | Higher (fewer cable losses) | Lower
Maintenance Access | Difficult | Easier
Installation Cost | Higher | Lower
Scalability for UK | High | Limited by grid capacity
System Complexity | High | Moderate
UK Suitability | High | Moderate
Table 2: Key parameter comparison of offshore vs onshore hydrogen production.

## Slide 6
Working Principle
Course: Research Dissertation (ENGM083)
Offshore
Wind Power Generation
Seawater Desalination
Electrolysis of water
Hydrogen Compression
Hydrogen Storage
Hydrogen Transportation
Figure 2: Working Principle of Offshore Green Hydrogen Production via Wind Powered Electrolysis.
6
Flow Chart of the whole working principle:

## Slide 7
Methodology
1
Literature Review
2
Selection of electrolyser
3
System Design & Boundary
4
Aspen HYSYS Simulation carried out mass and energy balance calculations
5
Techno Economic Analysis
6
Results and Discussion, Conclusions
Research approach and workflow:
Course: Research Dissertation (ENGM083)
7
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk

## Slide 8
Results Analysis Framework
Mass and Energy Balance
Simulation:
Aspen HYSYS stoichiometric reactor model.
Reaction: 2H₂O → 2H₂ + O₂ .
Techno Economic Analysis
Sensitivity Analysis
Wind variability.
Electricity cost.
Electrolyser performance.
Storage pressure (350 bar).
H₂ production rate.
Mass & Energy Balance and Techno Economic Analysis:
Course: Research Dissertation (ENGM083)
8

## Slide 9
Project Timeline & Deliverables
Course: Research Dissertation (ENGM083)
9

## Slide 10
References:
Aminaho, E.N., Aminaho, N.S. and Aminaho, F. (2025) ‘Techno-economic assessments of electrolysers for hydrogen production’ [Online]. Available at: https://www.sciencedirect.com/science/article/pii/S0306261925012450 (Accessed: 25 March 2026).
Carmo, M., Fritz, D.L., Mergel, J. and Stolten, D. (2013) ‘A comprehensive review on PEM water electrolysis’, International Journal of Hydrogen Energy [Online]. Available at: https://doi.org/10.1016/j.ijhydene.2013.01.151 (Accessed: 26 March 2026).
Ibrahim, O.S. et al. (2022) Dedicated large-scale floating offshore wind to hydrogen: Techno-economic and environmental assessment. Renewable and Sustainable Energy Reviews. Available at: https://www.sciencedirect.com/science/article/pii/S1364032122002258 (Accessed: 18 March 2026).
Niblett, D., Chiong, M.-C. and Zhang, Z. (2024) ‘Review of next generation hydrogen production from offshore wind using water electrolysis’ [Online]. Available at: https://www.sciencedirect.com/science/article/pii/S0378775323012806 (Accessed: 18 March 2026).
Ramakrishnan, S., Kolios, A., Cui, L. and Floros, M. (2024) ‘Offshore green hydrogen production from wind energy: Critical review and perspective’ [Online]. Available at: https://www.sciencedirect.com/science/article/pii/S1364032124000431 (Accessed: 01 April 2026).
Course: Research Dissertation (ENGM083)
10
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk

## Slide 11
Travaglini, R. et al. (2025) Offshore or onshore hydrogen production? A critical comparison of wind-to-hydrogen pathways. Applied Energy. Available at: https://www.sciencedirect.com (Accessed: 01 April 2026).
Wu, L., Xu, Y., Wang, Q., Zou, X., Pan, Z., Leung, M.K.H. and An, L. (2025) ‘Direct seawater electrolysis for green hydrogen production: electrode designs, cell configurations, and system integrations’ [Online]. Available at: https://pubs.rsc.org/en/content/articlelanding/2025/ee/d5ee01093d (Accessed: 18 March 2026).
Rezaei, M. et al. (2024) Techno-economics of offshore wind-based dynamic hydrogen production. Applied Energy. Available at: https://www.sciencedirect.com/science/article/pii/S0306261924014132 (Accessed: 25 April 2026).
Course: Research Dissertation (ENGM083)
11
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk

## Slide 12
Thank you !
Course: Research Dissertation (ENGM083)
12
Syed Yousaf Munib | 6933767 | sm04531@surrey.ac.uk